## Troubleshooting

Common troubles

In case a card key fails to open the lock, make sure to query the lock information using a summary card, carefully check the room-lock No., time, unlocking privilege, blacklist and unlocking records etc.

### A guest card fails to lock the door

| lamp | The green lamp | Glows | Circuit board wiring is loose | Reconnect it and try again | It means poor contact in wiring if it is normal during test |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | Circuit board wiring is normal | Replace the dead bolt assembly | Try again, if it is normal, it indicates that the motor or motor wiring has problems |  |  |
|  |  |  |  |  | Try again, if it is abnormal, it indicates that the circuit board has problems, replace the circuit board |  |  |
|  |  | Flashes | Once | The current guest card is disabled for the check-out room, for which a new guest card should be issued |  |  |
|  | Yellow lamp | Glows | No sound, it indicates mechanical double-lock | Open the lock with an emergency card | Try again, if it is normal, it indicates double-lock |
|  |  |  |  |  | Try again, if it is abnormal, it indicates that the microswitch of the dead bolt assembly has problems, replace the dead bolt assembly |
|  |  | Flashes | Sound indication | Beeps once | Guest serial No. in the lock is more than in the guest card. It needs to issue a new guest card or scan the Reset SN Card. |
|  |  |  |  | Beeps twice | Scan the locking card again to cancel the locking mode |
|  |  |  |  | Beeps thrice | Indicating that the guest card has been reported loss and disenabled, it needs to issue a new guest card |
|  | Red lamp | Glows | Once | Check if the guest card is within the effective time | Yes, - summarize and check the record in the lock, issue a time card and readjust the time of the lock |  |  |  |
|  |  |  |  |  | No, - The card is out of effective time, it needs to reissue a guest card |  |  |  |
|  |  | Flashes | Twice | Check if the room No. corresponding to the guest card No. is correct | Yes - summarize and check the record in the lock, issue a setting card and readjust the lock No. |  |  |  |
|  |  |  |  |  | No,- Readjust the guest card No. of the corresponding lock |  |  |  |

### A staff card fails to open the lock

| lamp | Green lamp | Glows | Circuit board wiring is loose | Reconnect it and try again | It means poor contact in wiring if it is normal during test |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | Circuit board wiring is normal | Replace the dead bolt assembly | If it is normal after reconnection, it indicates that the motor or motor wiring has problem |  |  |  |
|  |  |  |  |  | If it is abnormal after reconnection, it indicates that the circuit board has problems, replace the circuit board |  |  |  |
|  | Yellow lamp | Glows | No sound, it indicates mechanical double-lock | Open the lock with an emergency card | Try again, if it is normal, It indicates double-lock |  |  |  |
|  |  |  |  |  | Try again, if it is abnormal, it indicates that the microswitch of the dead bolt assembly has problems, replace the dead bolt assembly |  |  |  |
|  |  | Flashes | Sound indication | twice | Indicating that the room is locked by a locking card and cannot be opened by any card except an emergency card. Scan the locking card again to cancel the locking mode |  |  |  |
|  |  |  |  | thrice | Indicating that the guest card has been reported loss and disenabled, it needs to issue a new guest card |  |  |  |
|  |  | Glows | Once | Check if the staff card is within the effective time | Yes, - summarize and check the record in the lock, issue a time card and readjust the time of the lock |  |  |  |
|  |  |  |  |  | No, - The card is out of effective time, it needs to reissue a new staff card and reauthorize it |  |  |  |
|  | Red lamp | Flashes | twice | Check if the room No. corresponding to the guest card No. is correct | Yes - summarize and check the record in the lock, issue a setting card and readjust the lock No. |  |  |  |
|  |  |  |  |  | No,- Readjust the guest card No. of the corresponding lock |  |  |  |

### An emergency card fails to unlock the door

| lamp | Green lamp | Glows | Circuit board wiring is loose | Reconnect it and try again | It means poor contact in wiring if it is normal during test |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | Circuit board wiring is normal | Replace the dead bolt assembly | Try again, if it is normal, it indicates that the motor or motor wiring has problems |  |  |
|  |  |  |  |  | Try again, if it is abnormal, it indicates that the circuit board has problems, replace the circuit board |  |  |
|  | Red lamp | Glows | No sound | It is not a system card, check if the SP card is set correctly | Yes, - Replace the PCB and reset |  |  |  |
|  |  |  |  |  | Initialize the PCB and reset |  |  |  |

Sound and light indications

| Serial No. | Door lock operation | Lamp indication | Sound indication | Lock response | Result of the operation | Solving method |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Initialization | The green lamp glows | It beeps thrice | Non | Restore factory settings |  |
| 2 | Password Card | The green lamp glows | It beeps once | Non | Set the system password etc to the door lock |  |
| 3 | Locking card No. | The green lamp glows | It beeps once | Non | Set the No. etc to the door lock |  |
| 4 | Time card | The green lamp glows | “Beeps” once | Non | Set the door lock time and work time section into the door lock |  |
| 5 | Reset card | The green lamp glows | “Beeps” once | Non | Reset the guest information in the door lock |  |
| 6 | Room locking card | The green lamp glows | “Beeps” once | Non | After the room is locked by a locking card, it cannot be opened by any card except an emergency card. |  |
| 7 | Room locking card | The red lamp flashes | It beeps twice | Non | Clear the room locking ID and cancel the room locking |  |
| 8 | Check-out card | The green lamp glows | “Beeps” once | Non | Terminate the current guest, who can open the door |  |
| 9 | Open the door with a mechanical key | The green lamp glows | “Beeps” once | Unlock failure | An unlocking record is left |  |
| 10 | Open the door with a legal card | The green lamp glows | “Beeps” once | Open the door | The door is opened and an unlocking record is left |  |
| 11 | Close the door with a legal card | The red lamp glows | It beeps twice | Close the door | The door is closed |  |
| 12 | Enter/Exit Enabling mode: | Non | It beeps once (long) | Non | After the door is opened, scan the staff card with enabling function again during enabling, it indicated to enter the enabling mode. Scan the card again and exit |  |
| 13 | Enable the temporary card | Green lamp flash | It beeps once | Non | Enable the temporary card successfully under the enabling mode |  |
| 14 | Disable the temporary card | The red lamp flashes | It beeps twice | Non | Disable the temporary card successfully under the disabling mode |  |
| 15 | The temporary card is full | Non | It beeps thrice | Non | The temporary card is full if you enable it under the enabling mode |  |
| 16 | Inclined dead bolt alarm | The red lamp glows | I beeps thrice | Non | Locking failure | Inclined dead bolt alarm |
| 17 | Unlock under-voltage alarm | The green lamp glows | It beeps 8 times | Open the door | Battery voltage is low | Change the battery |
| 18 | Handset password setting | The green lamp glows | “Beeps” once | Non | Write the new password into the door lock |  |
| 19 | Setting lock allocation data with the handset | The green lamp glows | “Beeps” once | Non | Set the allocated data to the door lock |  |
| 20 | Read door lock time with the handset | The green lamp glows | “Beeps” once | Non | Read door lock time |  |
| 21 | Set door lock time with the handset | The green lamp glows | “Beeps” once | Non | Set door lock time |  |
| 22 | Query power status by the handset | The green lamp glows | “Beeps” once | Non | Query door lock power status | Replace the battery is under voltage is displayed |
| 23 | Summarize door lock information with the handset: | The green lamp glows | “Beeps” once | Non | Summarize door lock information |  |
| 24 | Non system card | The red lamp glows | Non | Unlock failure | Password error or card type error | Reissue the card |
| 25 | Ineffective card | The green lamp flashes and then the red lamp flashes | Non | Unlock failure | Verification error | Reissue the card |
| 26 | Mechanical double-lock | The yellow lamp glows | Non | Unlock failure | Except guest cards, other unlocking cards can be set to open or not open the door. |  |
| 27 | Time error indication | The red lamp glows | It beeps once | Unlock failure | There are 2 causes: 1. Ineffective guest card or staff card is scanned; 2. card operation error. |  |
| 28 | Lock No. error indication | The red lamp flashes | It beeps twice | Unlock failure | There are three causes: 1. Ineffective guest card or staff card is scanned; 2. card operation error. |  |
| 29 | Illegal card indication: | The red lamp flashes | It beeps thrice (long) | Unlock failure | Data error | Reissue the card |
| 30 | Check-out indication | Green lamp flash | It beeps once | Unlock failure | As the checkout card has disabled the current guest card, this signal appears if the current guest card scanned. | Issue a guest card |
| 31 | Old guest card indication | The yellow flash | It beeps once | Unlock failure | Scan the old guest card of the room ever stayed | Issue a guest card |
| 32 | Room locking indication | The yellow flash | It beeps twice | Unlock failure | Indicating that the room is locked by a locking card and cannot be opened by any card except an emergency card. | Scan the locking card again to cancel the locking mode |
| 33 | Loss report indication | The yellow lamp glows | It beeps thrice (long) | Unlock failure | A lost unlocking card that has been disabled is scanned | Cancel the loss report |
| 35 | Self-check of electrification | Press the key, it “beeps” long , it “beeps” short, the green lamp glows, it “beeps” short, the red lamp glows, , it “beeps” short, the yellow lamp glows, the motor rotates clockwise, the motor rotates counterclockwise |