Hand held unit instruction

Content

1. Hand held Unit	2

2. Hand held Unit profile	2

2.1. Function	2

2.2. Before Using	2

2.3. How to open and shut down	3

2.4. Manus of the hand held	3

3. Driver installation	3

4. Options operation	7

4.1. Change password of handset (change pw of handset)	7

4.2. Communicate with PC (communicate with PC)	8

4.3. Setup system password (setup sys pw)	17

4.4. Setup lock's information (setup lock's info)	17

4.5. Check lock's time (check lock's time)	17

4.6. Adjust lock's time (adjust lock's time)	17

4.7. Check lock's battery (check lock's battery)	17

4.8. Download lock's info (download lock's information)	18

# Hand held Unit

White wire for PC, black one for lock

# Hand held Unit profile

## Function

Hand held unit is used for setting lock, and audit trail the information, it will make you more convenient to setup the lock.

## Before Using

First, before using hand held, make sure SID card, all the rooms and members have been setup.

Second, our handheld is available for Win XP or Win Vista 32bit only, so before using that device, make sure you computer is Win XP or Win Vista 32bit.

## How to open and shut down

Turn on：Press "*" about 3 seconds. After one "beep", the LCD shows entry window meaning that handheld is on.

Turn off：Press "*" about 3 seconds. After one "beep", the handset is off.

## Manus of the hand held

When open the handheld, there is a Be-tech logo, Press "OK" key in entry window, and then follow the indication to enter the correct password and press "OK" key for logging in, you will see 8 options:

###### Change password of handset (change pw of handset)

###### Communicate with PC (communicate with PC)

###### Setup system password (setup sys pw)

###### Setup lock's information (setup lock's info)

###### Check lock's time (check lock's time)

###### Adjust lock's time (adjust lock's time)

###### Check lock's battery (check lock's battery)

###### Download lock's info(download lock's information

# Driver installation

Connect the handheld to the computer, and find out the “communicate with PC, there will be a screen pops up.

# Options operation

## Change password of handset (change pw of handset)

Function: The default password of handset is blank. After changing password of handset, users must access to handset with the correct password next time.

Operation: choose this option, press "OK", enter a new password, press "OK", confirm the new password, press "OK", done.

## Communicate with PC (communicate with PC)

Function: setup the handset on PC such as setting time, querying information, deleting date and so on.

Operation: connect with pc with appropriative line, and then choose this option, press "OK", done.

And the LED will show “Waiting for communication……”, if connection is faulty, it will show “connection failure”

Then go back to the software, find out the handset option, select “handset setting”

###### Set time

Set up handset’s time

###### Get time

Check handset’s time

###### Update SP

Update handset’s SID as software SID, it means that the handset must have the same SID with software, if their SID is different, the key cards issued for encoder could not open the door.

###### Delete data

Delete the old data of the handset, it will take about couples minutes.

###### Write handset

go to the software and find out “handset”, the choose “setting information”, you will see a screen as below shows, then choose “Locks”, “OK” for next.

When you press “OK”, you will see all rooms on the left, basically, we choose all room and move them to right, so you press “”

If you want to choose only one room, press “”

Press “next”

###### Time sections setting

Press “set”, you will many time sections you can set, it is like the “time card”, choose “Reset guest information” if locks are newly installed. And other two options depend on requirement.

###### Blacklist setting

if some card is lost, in that case, you need to choose the lost card, and take it into right, and that card can not be used as all the information is transmitted into the locks. Then, press “next”,

When you see “write handset successfully”, all the information of the hotel has been transmitted in the handset. The next step is going to set up the locks.

## Setup system password (setup sys pw)

Function ：Setup/change system password of the lock.

Operations:

Insert the USB-Mini USB wire, then go in front the lock, there is Mini USB socket at the bottom, connect handset with lock, then choose “ setup sys pw”---- “OK” ----“1 beep, green light” comes from lock, setting is successful. Then move to “setup lock’s info”

## Setup lock's information (setup lock's info)

Function: setup/change lock's information including lock's memory, motor's parameter, authorizing staffs, blacklist and so on.

Operation:

Choose “setup lock’s info”, press “OK”, you will see enter lock’s No., in that case, you can enter the locks’ No, and press “OK”, the lock’s No. is with 8 digits, the ahead 6 digits is same as “Door ID” in the software, and the last two digits are for inner door, without inner door is “00”, for example, if you want to find out the door ID is 100001 to set,  the Door ID in the software is 100001, there is no inner door in this room, so you enter 10000100; if there is one inner room in Door ID 200002, then you can enter 20000201 to find out that room No. And then, press “OK”----“1 beep, green light” comes from lock, done.

In another case, once you see “enter lock No.”, keep pressing “OK”, you will see all the rooms; find out the corresponding room, press “OK”----“1 beep, green light” comes from lock, done.

## Check lock's time (check lock's time)

Function：Check lock's current time.

Operation：Connect the lock with appropriative line, then choose this option, press "OK", done.

## Adjust lock's time (adjust lock's time)

Function：Set the current time to the lock.

Operation: connect with lock with appropriative line, and then choose this option, press "OK", confirm the time and press "OK", done.

This is another important step for setting the lock, it is used for setting lock’s time, then choose “ adjust lock’s time”---- “OK” ----“1 beep, green light” comes from lock, setting is successful, if you want to sure if the time has been set, you can use “check lock’s time”.

## Check lock's battery (check lock's battery)

Function：Check lock's current battery.

Operation：Connect the lock with appropriative line, then choose this option, press "OK", it will display normal/low.

## Download lock's info (download lock's information)

Function: download the current opening record of lock to handset

Operation: connect with lock with appropriative line, then choose this option, press "OK", wait for a moment, done.

Connect the lock with handset, choose the option, and press “OK”, it will take couples seconds to download the information from the lock.

After downloading the information, connect the handset with PC, and choose “communicate with PC”,

Go back to the software, find out the “Handset”, and choose “query information”, you will see the screen as below, and them press “OK”.

Press “read data”

Press “Yes”.

Notice: Do not move the device or load any other operation in PC when downloading the information.

After downloading the information, you will see the screen as below, click the room you want, and then press “Query”,

When “Read handset successfully” pops up, press “OK”, you will see another screen as below,

Choose the room and right click the mouse, and you will see “view”,  press “view”, finally, you can see all the information of the lock.

Notice: one handset can download several locks’ information. But need to view the information one by one.